Extending the Capabilities of the
Transverse Multibunch Feedback Processor at Diamond
Michael Abbott, Diamond Light Source
Libera Workshop 2014
10th April 2014

---
TMBF in Context
Storage Ring
EBPM button block
Striplines
X
Y
Power Amplifier
Hybrid
A
B
C
D
Y
Σ
Q
X
Power Amplifier
TMBF Front End
Machine RF
Libera TMBF (X)
Libera TMBF (Y)
[Speaker Notes: This and the following slide go together and say much the same thing]

---
TMBF Processing Framework
- Button pickups for ABCD RF signals
- RF hybrids convert to X & Y
- Libera TMBF front end for signal conditioning
- 4 x 125 Ms/s 14-bit ADC in Libera TMBF
- FPGA performs processing and control
- 1 x 500 Ms/s 14-bit DAC in Libera TMBF
- Power Amplifier drives striplines to couple back to stored beam

---
Libera TMBF
Xilinx Virtex-II Pro FPGA
i-Tech FPGA framework
DLS
FPGA
Code
DAC
ADC
4 x 14
500 Ms/s
14 bit / sample
4 x 125 Ms/s
14 bit / sample
128 MB
DDR
RAM
Triggers
XScale ARM SoC
64 MB RAM
32 MB Flash
100 Mbit
Ethernet
[Speaker Notes: Talk about FPGA resources and i-Tech framework. Point out need for framework sources to make needed local modifications. Perhaps also point out 4 to 1 speed mismatch and associated issues. Extra slide on FPGA resources?]

---
TMBF Applications
- Instability damping: simple tuned FIR to reverse phase for negative feedback. Works well in part due to very sharp resonance of beam at machine tune frequency.
- Tune measurement by tune excitation and detection
- Machine physics investigations: probing instabilities
[Speaker Notes: General context of TMBF]

---
Top Level EPICS Control

---
New TMBF Capabilities
- Bunch-by-bunch control of filter, output, gain.
- Three output sources: FIR, two NCOs
- Programmable sequencer
- Tune following PLL
- Output pre-emphasis filter, input compensation to come
- 2ns resolution triggers and synchronisation
- Compensation for all offsets and delays
[Speaker Notes: This is why we're here: all the new stuff. Was originally a very small upgrade project, but took off as we discovered more capabilities and Guenther came up with more ideas.]

---
Architecture and Implementation
- Split between EPICS IOC (written in C) and FPGA (written in System Verilog)
- Offset and delay compensation in software where possible: 19 delay parameters automatically measured and compensated
- Libera platform provides SBC, DDR RAM, ADC, DAC. Everything else in DLS code

---
19 Compensated Delays
# DDR readout delays
DDR_ADC_DELAY = 230
DDR_FIR_DELAY = 1
DDR_RAW_DAC_DELAY = 5
DDR_DAC_DELAY = 10
# Buffer trigger delays
BUF_ADC_DELAY = 229
BUF_FIR_DELAY = 0
BUF_DAC_DELAY = 9
# MinMax buffer delays
MINMAX_ADC_DELAY = 228
MINMAX_DAC_DELAY = 8
# Bunch selection offsets
BUNCH_FIR_OFFSET = 228
BUNCH_GAIN_OFFSET = 0
# Detector single bunch offsets and phase
# skews
DET_ADC_OFFSET = 1
DET_FIR_OFFSET = 232
# These two values represent actual phase
# delays in bunches relative to an
# aligned single turn.
DET_ADC_DELAY = 0
DET_FIR_DELAY = 12
# Tune following delays
FTUN_ADC_OFFSET = 3
FTUN_FIR_OFFSET = 0
FTUN_ADC_DELAY = 928
FTUN_FIR_DELAY = 940
All measured automatically when testing a new FPGA version

---
FPGA System Overview
Loopback for Debug
FIR
input
FIR
output
ADC
DAC
NCO1
NCO2
DAC
capture
FIR
sequencer
&
detector
bunch
control
ADC
ADC
IQ
FIR
tune PLL
ADC
FIR
[Speaker Notes: Architectural overview of new system implementation showing the available system resources.]

---
Data Capture
min/max
ADC
min/max
DAC
DDR
RAM
64M x 16
ADC
FIR
DAC
block
RAM
16k x 16 x 2
2 of 3
IQ

---
Output Control
Overflow
Detect
0
Off
FIR
NCO1
FIR+NCO1
NCO2
FIR+NCO2
NCO1+NCO2
FIR+NCO1+NCO2
FIR
NCO1
pre-
emphasis
FIR
delay:
0-935
+
×
NCO2
DAC
+
+
+
capture
Output
Select
Output
Gain
Bunch by bunch
control

---
A Fragment of FPGA Code
// DAC selection input multiplexer. The intermediate selection is 16 bits wide
// so we can detect overflow when adding up to three 14 bit values.
logic [7:0] [15:0] dac_out_mux = 0;
always_ff @(posedge adc_clk_i) begin
    dac_out_mux[0] <= 0;
    dac_out_mux[1] <= signed'(fir_dat_i);
    dac_out_mux[2] <= signed'(hom_0_dat_i);
    dac_out_mux[3] <= signed'(hom_0_dat_i) + signed'(fir_dat_i);
    dac_out_mux[4] <= signed'(hom_1_dat_i);
    dac_out_mux[5] <= signed'(hom_1_dat_i) + signed'(fir_dat_i);
    dac_out_mux[6] <= signed'(hom_1_dat_i) + signed'(hom_0_dat_i);
    dac_out_mux[7] <=
        signed'(hom_1_dat_i) + signed'(hom_0_dat_i) + signed'(fir_dat_i);
end
wire [15:0] dac_out_sel = dac_out_mux[out_mux_sel_i];
// Latch final result and detect overflow
logic [13:0] dac_mux_out = 0;
logic mux_overflow = 0;
always_ff @(posedge adc_clk_i) begin
    dac_mux_out <= dac_out_sel;
    mux_overflow <= ~&dac_out_sel[15:13] & |dac_out_sel[15:13];
end

---
Bunch by Bunch Control
- Different feedback on different bunches, helpful for unusual fill patterns
- Precise control over tune sweeps (can measure up to four channels at once)
- Low risk user time experiments on a single bunch (nobody cares too much if we break one bunch!)
[Speaker Notes: This was the first major capability upgrade.]

---
Bunch Control
Current bunch configuration
FIR select
(one of 4)
Bank select
from
sequencer
Output select
(8 options)
Output gain
(range ±1023)
Sequencer selects one of four bunch control configurations. Selected configuration determines bunch by bunch behaviour.
Bunch configuration:
for each of 936 bunches selects:
FIR (2 bits)
output (3 bits)
gain (11 bits).
Bunch counter,
advances every
2ns
[Speaker Notes: This needs some explanation! The 8 output options are any selection from three outputs (FIR and two NCOs).]

---
Tune Measurement
- Excite system under test with fixed frequency sin wave
- Measure response by mixing with original excitation: use both phases to get IQ response
- Sweep excitation frequency to get response over a frequency range
device
under
test
cos
detector
∿
IQ
cos,sin

---
Detector Features
- Blanking signal. External signal during injection to suspend detector during injection to avoid spurious noise.
- Window. Windowing sine wave that doesn't fit into detector window controls leakage from adjacent frequencies:
⨯

---
Tune Measurement Screen

---
Sequencer and Detector
DETECTOR
Σ
gain
I
×
ADC
×
IQ
FIR
Q
×
write IQ
blanking
event
NCO
NCO
cos
gain
NCO1
sin
frequency
gain
sequencer
window
bank
select

---
Programmable Sequencer
For tune sweeps and timed feedback control experiments. For up to 7 sequenced states can select:
- Bunch configuration from one of four selections
- Frequency sweep for NCO
- Optional IQ data capture for sweep response
- Duration of state
[Speaker Notes: This is the other major upgrade and the one with the most complex implications.]

---
Sequencer Programme
Start on trigger
N state programme
State0
StateN
…
State1
State0
COUNT = C1
DWELL = D1
HOLDOFF = H1
Dwell0
Dwell1
...
DwellC-1
f1
f1+δf1
f0+(C1-1)δf1
H1 Turns
D1 turns: detector active
H1+D1 Turns
detector window
[Speaker Notes: Structure of a sequencer programme: a sequence of states, each state consisting of a sequence of dwells at each frequency as the NCO frequency is swept, each dwell consists of an optional holdoff followed by a detector capture period. Each dwell results in the capture of one (optional) IQ point.]

---
Sequencer Applications
- Tune sweep: one extra state with sweep
- Complex machine investigations. For example, grow/damp exploration of unstable modes, can perform the following experiment:
  - Running in feedback with standard feedback
  - Turn feedback off, excite one mode for 100 turns
  - Wait for natural growth of mode, eg 1000 turns
  - Run an alternate feedback filter for 1000 turns
  - Restore standard feedback, capture 1000 turns
[Speaker Notes: Sweeping, or all the complicated ideas that Guenther wants. This is just a slightly contrived example application.]

---
Implementing Grow/Damp
State #	FIR	Output	Duration	Dwell time	Bank #
0	Standard	FIR	-	-	0
4	-	Sweep NCO	100	1	1
3	-	Off	1000	1	2
2	Alternate	FIR	1000	1	3
1	Standard	FIR	1000	1	0
0	Standard	FIR	-	-	0
Here we use four out of seven available sequencer states, two of four available feedback filters, and all four available bunch control banks.
The result of this experiment is 3100 IQ sample points.
Can also simultaneously capture turn by turn data into the fast DDR buffer if desired, have room for up to 35,000 turns in the buffer, but readout is relatively slow, around 1,200 turns per second.
[Speaker Notes: Digging into the contrived example to illustrate how the sequencer is designed to be used.]

---
Graph of a Grow/Damp Experiment
Excite at tune and
selected mode
for 500 turns
Feedback off,
observe natural
damping
Feedback
restored
[Speaker Notes: A rather rough snapshot from a recent grow damp experiment (alas, not the four state one I was describing). Cleaner data would be nice...]

---
Low Level Control Screens

---
Tune Measurement
Peak response
at tune frequency
Synchrotron
sidebands
Note rapid phase change
when sweeping through
peak of resonance

---
Tune Phase Locked Loop
- Take advantage of rapid phase change through tune frequency peak
- Measure phase at, eg, 2.6 kHz (every 200 turns)
- Run simple controller to track frequency to keep phase at target value
- Result is high update rate tune measurement
- Can quickly measure tune width by stepping phase through ±45°

---
Tune Phase Locked Loop
detector
CORDIC
ADC
IQ
phase
reference
phase
−
FIR
phase
error
cos,sin
NCO
NCO2
IIR
{2^{-N}} over {1 - (1-2^{-N})z^{-1}}
frequency correction
+
PI controller
KI
KP
×
×
buffer
reference
frequency
Σ
+

---
Tune PLL Screen
BBA orbit changes
cause changes in tune

---
First PLL Tune Measurements
5, 10, 15 Hz, etc – injection?
Mains (50 Hz, 100 Hz)
3, 6, 9, 12 Hz, etc –
mystery signal, not seen
before this measurement
Long term 71.2 Hz signal
Believe comes from one
steerer, have seen this
signal for several years!
Broadband low frequency,
comes and goes.
Ground motion?
Controller mistune?
Controller rolloff

---
Output Pre-Emphasis
- Loss of gain at high frequencies from DAC, Amplifier, ADC
- Can partially compensate with 3-tap FIR in DAC output
- Will also add 3-tap FIR to ADC input to compensate ADC high frequency droop

---
Closed Loop Gain Compensation
Filter coefficients: +1.323 -0.485 +0.162

---
2ns Trigger Synchronisation
- FPGA runs with 8ns cycle: 4 machine bunches per tick
- Need to identify which bunch is synchronous with incoming trigger
- Need to identify trigger edge with 2ns precision

---
Discovering Trigger Edge
DDR
A
D-DDR
φ
φ
2φ
B
Trigger
Trigger with phase detect
φ
φ
C
2φ
φ
φ
D
φ
φ
A
B
C
D
A
B
C
D
Here we see ABCD go from
0000 to 0011 and can infer precise phase of trigger edge
0
0
1
1
0
0
0
0
φ
φ
φ

---
FPGA from a software perspective
- You need a helpful FPGA expert! Isa's help and advice was invaluable
- Completely different mind set: everything happens at once, not in sequence
- Open tools are practically nonexistent, entire philosophy is very bound to vendors
- System Verilog a horribly flawed language
- Timing constraints always a perpetual problem
- Solve problems with more pipelining!

---
Conclusions
- Developing driver software and FPGA together: very satisfying and flexible
- Many many thanks to:
  - Isa Uzun for first version of FPGA and lots of advice
  - Guenther Rehm for detailed steering, guidance, many ideas, and in-depth evaluation
  - Graham Naylor for initial FPGA design
  - I-Tech for the Libera TMBF platform